## Slide 1
COMPONENTS OF FIRE
Oxygen [Air]
Fuel
Ignition Source(Heat)
Fire Triangle
Fuel
Oxygen
Ignition
Source
There are four classes of fire
Class A - Ordinary combustibles (water)
Class B – Flammable liquids, gasoline(Smothering)
Class C – Combustible gas
Class D – Electric Fire
Fire extinguishers are designed to cope with fires
in their incipiency, and generally designed by the
class of fire they are to control[A, AB&C,BC etc.]
Improper Electrical Connections-
cable sizing / overload
Hot works
Leakages-gas
Poor Housekeeping
Uncontrolled Smoking
etc
Causes of Fire
BASIC FIRE FIGHTING TECHNIQUES
P&G[WEST AFRICA]-IBADAN
.
Following hot work permit
Good housekeeping
Inspection
Proper electrical connections
Flammable liquids storage
Empty pallets storage
Smoking control
Change Control
etc
Fire Prevention
FIRE FIGHTING EQUIPMENT
The plant fire fighting equipment include:
1. Portable & mobile / wheeled extinguishers
2. CO2 flooding system
3. Deluge & Sprinkler system[ Dust Filters]
4. Hose reels and hydrant
WATER EXTINGUISHERS [ for Class A]
        DRY POWDER [A,B,C&D}
These are of two types.
‘‘ABC’’ Dry chemical
“BC’’ Dry chemical
They are both multipurpose extinguisher that can
be used on all classes of fire [A,B&C]
Cylinder color BLUE or Red
Capacity 9kg.
CARBON DIOXIDE [for B & C]
Cylinder color BLACK
Capacity 5 & 9kg
Steps to follow in using fire extinguisher.
1. Remove appropriate extinguisher from the hanger.
[ After identifying the type of fire]
2. Hold the cylinder in upright position.
3. Remove the seal.
4. Remove the lock pin.
5. Keep a relatively safe distance from the fire
6. Hold the nozzle and direct it at the base of the fire.
7. Squeeze the lever.
NOTE : After extinguishing the flame, direct the stream at
smoldering or glowing surfaces.
The effectiveness of CO2 will be nullified if used in a strong
windy area.

## Slide 2
Safety Map Creation
Objective of safety maps:
To provide a visual display of the hazards present on a piece of
equipment and to document the countermeasures which should be
applied to minimize the risk.
Process:
Identify the Sources of Energy and Hazards of your equipment.
Identify the safety equipment and devices, that protect from the identified hazards.
Identify the personal protective equipment that protect the people in case an incident happen.
The intent behind a safety map is to point out all the potential hazards.
Safety Maps should be:
1. Equipment specific
Both of these machines do the same thing but are completely different.
The same safety map will not be suitable for both!
2. Permanently available at the piece of equipment.
3. Up to date and updated as the equipment is modified.
Colour coding:
Colour code the edges of all symbols used on the safety map following
a similar standard to below – colours used need to be consistent across
the site.
Red is used to identify sources of energy and hazards
Green is used to identify safety devices (e.g. isolators)
Blue is used to identify PPE requirements

## Slide 3: KE I Leadership & Commitment
HSE KEY ELEMENTS
WHO? Everyone Including You
WHAT? Make sure you:
Know your HS&E expectations
Read and follow recommendations found in routine HS&E communications
Reinforce safe practices with co-workers
KE II Risk Assessment, Design and Construction
This Key Element has four sub-elements:
Process Systems
Utility Systems
Health and Safety Systems
Environmental Systems
KE III Operation & Maintenance
WHO? HS&E Leadership and You
WHAT? Make sure that you:
Set and follow proper Operation & Maintenance Procedures
Provide and obtain training on proper procedures
Ensure inspections and maintenance are completed
Key Element III has four sub-elements:
Process Systems
Utility Systems
Health and Safety Systems
Environmental Systems
KE IV Training & Procedure
WHO? Everyone including you
WHAT? Obtain proper training BEFORE you do any job. In some cases, you may be required to obtain medical clearance before doing specific tasks (e.g., Lift truck operation requires that you have your eyes tested.)
WHO? Site HS&E Leadership, Technical Resources, with assistance from you as requested
WHAT? Make sure you:
Evaluate the potential HS&E hazards
Design equipment and systems to address hazards
Ensure proper construction of systems
Provide input on proper operation and maintenance
KE V Behavior Observation and Feedback
WHO? Everyone including you
WHAT? Provide your co-workers with on-going feedback on safety behaviors (Both Safe and Unsafe
Worldwide statistics show Unsafe Behaviors cause the majority of ALL Injuries.
Use of the Behavior Feedback System at P&G has decreased the injury rate significantly.
KE VI Prevention & Improvement
WHO? Everyone including you
WHAT?
Know and follow Site Emergency Response plans, including evacuation procedures
Participate in correcting unsafe conditions in hazard or condition audits as requested.
Report all incidents. If you are injured, report to your team leader and seek medical attention immediately. You are also required to report near misses.
Make no changes to processes, procedures, equipment or introduce new chemicals to the workplace without receiving proper authorization.

## Slide 4: Operational Guidelines Compliance
BASIC ENZYME HYGIENE QUALIFICATION
WHAT ARE ENZYMES?
  Protein molecules
  Effective catalysts
  Biodegradable
  Very specific
  Used in lot of industrial applications
  Not living organism
  Not Chemicals
ENZYMES BEING USED IN IBADAN
  Purafect
  Celluclean
  Stainzyme
  Mannanase
  Calipso
ENZYMES ARE EFFICIENT AND COST-EFFECTIVE
Enzymes are very efficient catalysts
Only a SMALL amount of enzyme being used in our products gives high
Routes of exposure :
  Inhalation
  Ingestion
  Absorption
  Injection
Primary route of concern is inhalation
SKIN AND EYE IRRITATION
Due to the irritant nature of the enzymes
Can be prevented by :
  Improved personal hygiene
  Use of PPE
Enzymes are not skin sensitizers
Grade 3
Grade 2
Grade 1
Grade 0
Lower respiratory responses -
asthma type symptoms
Upper respiratory responses -
hay fever type symptoms
Sensitization – no symptoms
No effects
Enzymes are KEY INGREDIENTS
Our business depends upon our capability of using
the existing enzymes in our products AND
introducing new & better performing ingredients
in the future.
The HYGIENE PROGRAM allows us to meet
these business needs.
MOST POWERFUL PREVENTION TOOL!!!
No visible dust/aerosol
No recurring spillages
Treat empty containers as if full
No gross skin contact/Clothing Contact
Use TAUU rating for OGC 4. Target
3. Acceptable
2. Unacceptable
1. Unacceptable
GLOBAL ENZYME MANAGEMENT SYSTEM (GEMS)
<3% Sensitizations
No Grade 2 or Grade 3 Reactions.
Exposure Control
Operating Standards
Medical Surveillance
Leadership, Behavior and Culture
Exposure Assessment

## Slide 5
SPILLS HANDLING
“You can’t Get Sensitized,Unless you Get Exposed!”
Clean—Care—Fit-----Wear
Clean your respirator at least once per day!
Inspect all valves and elastics at least once per week!
Do a positive and negative fit check every time you wear the respirator!
Wear the respirator when needed!
On a regular basis, the major parts of the respirator (e.g. straps, exhalation valve, respirator housing) need to be inspected. Below the components of the half-face mask. Other respiratory protection also requires maintenance!
How to conduct a positive/negative fit test?
*Positive: Place the palm of the hand over the exhalation valve cover and exhale gently. If the face piece bulges slightly and no air leaks
between face and face piece are detected, a proper fit has been achieved.
*Negative: Place the palm of your hand over the central indentation of the filters, inhale gently and hold your breath for five or ten seconds. If the face piece collapses slightly and you feel resistance, a proper fit has been achieved.
  Do not touch mask with gloves , assume gloves always contaminated
  Never store gloves in same sack as mask
  Use gloves when potential for touching finished product
  Contaminated coveralls need to be changed. Wear disposable suit for high exposure tasks (e.g. riddling, washing, large maintenance)
  Wash hands immediately after all skin contact.
Site Employees
  Half face mask with P3 filter
  Medically qualified
  Fit-test prior to initial use
  Fit-test prior to each use
  Annual fit-test for all users
  Wear according to PPE Matrix, JSP, …
  Carry respirator at all times in operation areas
No visible dust
  No visible dust/powder
    No respirator required
  Light clouds of visible dust
    Half face mask with HEPA filter
  Major dust cloud (on-going/job)
    Wear PAPR (+ other PPE)
  Major peak exposure
    Wear PAPR (+ other PPE)
3M USAGE LINKED TO OGC
Fanning action